## Slide 1
This is currently the most popular hybrid inverter in the Eropean market, he can be connected to the grid operation, or not connected to the grid operation. With six charging and discharging period, it can also accept the energy stored by a diesel generator t keep your home powered for 24 hours a day.

## Slide 2
Model SUN-12K-SG01LP1-EU SUN-14K-SG01LP1-EU SUN-16K-SG01LP1-EU |  |  | 
BatteryType | Lead-acid or Li-lon |  | 
Battery Voltage Range (V) | 40~60 |  | 
Max. Charging Current (A) | 220 | 250 | 290
Max. Discharging Current (A) | 220 | 250 | 290
External Temperature Sensor | Yes |  | 
Charging Curve | 3 Stages / Equalization |  | 
Charging Strategy for Li-Ion Battery | Self-adaption to BMS |  | 
PV String Input Data |  |  | 
Max. DC Input Power (W) | 15600 | 18200 | 20800
Max. DC Input Voltage (V) | 500 |  | 
Start-up Voltage (V) | 125 |  | 
MPPT Range (V) | 150-425 |  | 
Rated DC Input Voltage (V) | 370 |  | 
PV Input Current (A) | 26+26+26 |  | 
Max. PV ISC(A) | 44+44+44 |  | 
No.of MPP Trackers | 3 |  | 
No.of Strings per MPP TrackerAC Output DataRated AC OutputPower (W) | 2 |  | 
 | 12000 | 14000 | 16000
AC Output Rated Current (A) | 54.5/52.2 | 63.6/60.9 | 72.7/69.6
Max. Continuous AC Passthrough (A) | 100 |  | 
Peak Power (off grid) | 2 time of rated power, 5 S |  | 
Power Factor | 0.8 leading to 0.8 lagging |  | 
Output Frequency and Voltage | 50/60Hz; L/N/PE 220/230Vac (single phase) |  | 
Grid Type | Single Phase |  | 
DC injection current (mA) | <0.5%1n |  | 
Backup Data |  |  | 
Backup Power (W) | 10000 | 12000 | 14000
Backup Rated Current (A) | 45.5/43.5 | 54.5/52.2 | 63.6/60.9
Backup UPSEfficiencyMax. Efficiency | 6ms Automatic switchover time 97.60% |  | 
Euro Efficiency | 96.50% |  | 
MPPT Efficiency Integrated | 99.90% PVInputLightningProtection,Anti-islandingProtection,PVStringInputReversePolarityProtection, InsulationResistorDetection,ResidualCurrentMonitoringUnit,OutputOverCurrentProtection, OutputShortedProtection,Surgeprotection |  | 
Output Over Voltage ProtectionCertifications and StandardsGrid Regulation | DC Type II/AC Type III CEI 0-21, VDE-AR-N 4105, NRS 097, IEC 62116, IEC 61727, G99, G98,VDE 0126-1-1, RD 1699, C10-11 |  | 
Safety EMC / StandardGeneral DataOperating Temperature Range (℃) | IEC/EN 61000-6-1/2/3/4, IEC/EN 62109-1, IEC/EN 62109-2 -40~60℃, >45℃ derating |  | 
Cooling | Smart cooling |  | 
Noise (dB) | <30 dB |  | 
Communication with BMS | RS485; CAN |  | 
Weight (kg) | 48.5 |  | 
Size (mm) | 464W×798.4H×300D |  | 
Protection Degree | IP65 |  | 
Installation Style | Wall-mounted |  | 
WarrantyFeatures | 5 years |  |